# Text boxes

Substation

Footbridge

Comm. Ctr. Building

Start/ / Finish

GRASS

FIELD

Util pole/guy wires

Community

Watch sign

Sycolin Rd SE

Lawson Rd

Rte 15 Overpass

W&OD Trail

W&OD

Trail

Tuscarora Creek Park Trail

Pedestrian path

Transportation Dept.

TURNAROUND

N

4.3 meters

Sign

Cone

4.3 meters

Util pole w/guy wires

Pine tree

Cedar

tree

50 feet

Start/Finish

Footbridge

48.5 ft

(Range w/green paint

mark on footpath)

N

START/FINISH DETAIL

DOUGLASS COMMUNITY CENTER 5K

Leesburg, VA

MAP NOT TO SCALE

(1)

(2)

(3)

MEASURED POINTS                                           Restrictions:  None

Start/Finish:  On grass field W of pedestrian path; E-W line between cedar tree on E side of field 48.5 ft  N of bridge, and pine tree on W side of field by substation fence, 50 ft. S of base of PVC-covered guy wires at pole at N end of substation.

Mile 1:  S side of W&OD Trail, 100 meters (~330 ft) W of STOP bar at Lawson Rd crossing, t pavement crack; in line w/ E end of scaffold next to long building at Transportation Dept. property on N side of trail.

Turnaround:  W&OD Trail, 4.3 meters (~14 ft) E of Community Watch sign at junction of Tuscarora Creek Park Trail.

Mile 2: N side of W&OD Trail, 59 meters (~194 ft) E of Lawson Rd; in line w/ 12” dia. tree; 18.4 meters (~61 ft) E of crosswalk at Stop warning sign.

Mile 3: N side of W&OD Trail, 86 meters (~282 ft) E of junction of Douglass Community Park Trail and W&OD Trail,  ~10 meters (~33 ft) E of pile of fallen trees on N side of trail.

Elevation

Start/Finish:  305 ft      Highest:  305 ft     Lowest:  256 ft.

Measured for certification by Liza Recto on August 18, 2013

Pine tree

Cedar tree

Run directly  from Start and across footpath to W&OD Trail (86.1meters)